6/19/2017

## 7 Rules of Rigging

As chaotic as life seems at times one can find order if he or she takes a closer look at the situation. This is true for rigging activities as well. If you follow the following 7 Rules you will always be on the safe side during your rigging activities.

- Know the load weight.

- Locate or estimate the location of the load's Center of Gravity (CG).

- Determine the load-share on each side of C/G.

- Calculate the tension in each sling-leg.

- As a minimum, select slings with capacity to match the sling-leg tension and hardware to match the vertical capacity of the slings.

- Inspect the rigging per ASME B30.9 and 29 CFR 1910.184.

- Ensure Great Load Control. Make sure the hitch or hitches you have selected, and their edge protection, provide good to excellent control so slipping does not occur.