5/20/2019

- Print

- Email

Ladder Safety

Set Up and Use of a Ladder

A major cause of falls from ladders is improper set-up. Many accidents can be avoided with common sense and good work practices. Using proper set-up techniques will give your ladder maximum stability and help ensure your safety.

PREPARING TO USE A LADDER

Your first step is to rid the area of hazards.

• Look above for any overhead wires or obstructions.

• Use non-conductive ladders for all electrical work.

• Clear any clutter from the area around the base of the ladder.

• Block off the area around the ladder so people and equipment won’t knock you off the ladder.

• If you’re working close to a corner, put a sign to warn people of your presence.

• If there’s a door nearby, lock it, block it off, or station someone to watch it for you.

• Before you use a ladder, check its rating. And be sure not to subject it to a load greater than its rated   capacity.

USE OF A LADDER

• Position a ladder carefully to prevent slipping.

• Where slipping is likely, tie off or have someone hold the ladder in position.

• Do not use a ladder for anything other than its stated purpose.

• Do not use boxes, barrels, or other objects to raise a ladder higher.

• Do not place ladders in front of doors opening toward the ladder unless the door is blocked, locked, or guarded.

• Position the base of an extension or straight ladder one foot away from the wall for every four feet of the ladder’s length from the support point to the surface.

• Before climbing onto a roof using an extension ladder, be sure the ladder extends three feet beyond the roof line.

• Never overextend an extension ladder.

• Read and follow all instructions on the ladder.