8/16/2019

## Basic Excavation Safety Talk

According to the Bureau of Labor Statistics there were 250 excavation related fatalities from 2009 to 2017. Excavations are common on construction sites all across the United States, but excavation work can be made safe by following basic safety guidelines.

Some major hazards of excavations:

- Cave in and collapses

- Water accumulation

- Falls into the excavation

- Utility strikes

- Poisonous gases collecting in an excavation

### Ways to Mitigate Excavation Hazards

- Follow OSHA’s guidelines for protective systems to protect employees entering the excavation. Often times the soil being excavated is referred to “Type C” which is the most hazardous for employees to enter. Excavations should be sloped back according to OSHA’s guidelines which depends on the soil type present. Trench boxes and shoring are other options to protect employees entering the excavation.

- Prohibit equipment and other employees from working above anyone working in the trench or excavation.

- Keep water out of the excavation. Use pumps to remove water from the excavation and do not allow employees to be in any excavation or trench that has water accumulating in it. Water affects the integrity of the excavation.

- Never leave the excavation open when work is not being performed in the area. Use barricades, fencing, and signage to protect both employees and anyone passing by from falling into the excavation or driving into it.

- Always use the “One Call” service in your area to ensure there are no utilities in proposed excavation areas or have utilities properly marked prior to digging. Look at as built drawings when they are available for the area the excavation is occurring.

- When there is a chance for a hazardous atmosphere in an excavation and individuals have to enter it ensure gas testing is done including any low points where gases can collect.

Toolbox talk based on NMGC submitted by Harry Simpson – Paulsboro Refinery

Summertime heat is not often looked at as a major threat; it just does not cause the destruction like tornadoes, floods, or hurricanes. But in reality, excessive heat is deadly, killing more than a hundred Americans per year. That is more than hurricanes, lightning, tornadoes and flooding.

What is the Heat Index?