8/5/2019

Aerial Work Platform Safety

Man-lifts and scissor lifts are two pieces of equipment that many workers can’t imagine working without. This equipment, if used correctly, provides quick and safe access to work areas that at one time could only be reached from scaffolding or a crane’s man-basket. These lifts, collectively called Aerial Work Platforms, are important tools. But as with any tool, there are right and wrong ways to use them safely.

The most important tip to remember before operating any aerial lift platform, is to always read and follow the manufacturer’s safety and operation manual! This information must be kept on the rig, and can usually be found in a PVC tube that’s tied to the machine’s frame or rails.

Safe operating procedures for both man-lifts and scissor lifts:

- Only trained and authorized people should operate the lift. A qualified instructor must make sure that every operator reads and/or understands the equipment’s safety and operating instructions. This includes all of the warning decals and labels mounted on the machine.

- Always check for overhead obstructions before driving or elevating the platform.

- Refuel tanks only when the unit is turned off. If battery powered, the batteries should be charged only in a well- ventilated area, away from any open flame.

- Prior to each shift a safety inspection should be completed by the operator; this includes both a visual inspection and a function test. If a problem is found, get the lift repaired.

- Elevate the platform only when it is on a firm, level surface. Although many lifts look like a rough terrain piece of equipment, they are not. Their large tires do allow the equipment to access somewhat difficult areas, but once in position they are designed to be out of level only 5 degrees while in operation. This amounts to 10 inches in a 10 foot wheel span. In addition, the lift must have a tilt alarm that activates when the machine is more than 5 degrees out of level.