9/16/2019

Electrical Safety

Extension Cords

1. Extension cords shall be suitable for the intended environment and

voltage and shall be listed by an appropriate product safety testing and

certification organization. All extension cords must be of the three-wire type.

Extension cords must be designed for hard or extra hard use at 14/3 or 12/3

gage, rated for 15 Amps.

2. Extension cords shall be assembled and tested by a

qualified electrician. Splices are not permitted in extension cords.

3. Extension cords shall not be used as permanent wiring.

4. Extension cords shall be protected from mechanical damage, oil,

solvents, abrasion, pinch points and sharp objects, vehicles and pedestrians.

Worn, frayed, oil soaked electrical cords and cables shall not be used.

5. Extension cords shall be placed so they do not cause slip, trip, or fall

hazards.

6. Extension cords shall be secured or suspended using non-conductive

means. Extension cords shall not be fastened with staples, hung from nails,

or suspended by wire.

7. All extension cords shall be visually inspected prior to each use. Any

worn, frayed, damaged, crushed, pinched, spliced or defective extension cord

shall be immediately removed from service.

8. Documented inspections of extension cords shall be performed per the

requirements of local regulations or consensus standards.

9. Extension cords shall not be unplugged while the equipment is operating.

10. Extension cords supplied from a disconnect switch shall not be unplugged with the disconnect switch closed.