9/9/2019

Electrical Safety

Ground-Fault-Circuit-Interrupters (GFCI)

1. Each location shall conduct a survey to determine, per local regulations or

consensus standards, all circuits requiring the installation of GFCIs.

2. Anytime an extension cord set is used, the extension cord set shall be

protected by a GFCI.

3. GFCIs shall be used anytime extension cord sets are used for construction or

maintenance tasks.

4. Portable GFCIs used in construction and maintenance activities shall be

inspected and tested prior to each use. Any damaged GFCIs shall be

immediately removed from service.

5. Permanently mounted GFCIs, shall be inspected on a quarterly basis and/or

according to the manufacturer’s instructions.

6. A portable GFCI shall be plugged directly into a receptacle and an extension

cord shall be plugged into the portable GFCI. Ensure that hands are not wet

when plugging or unplugging cords.

7. Ground fault circuit interrupters (GFCIs), low voltage, and/or double-insulated

tools will be used in construction and wet locations and on all extension cord

fed portable power tools.