01/17/2020

SPOTTERS

I'm sure everyone here is aware of the dangers of blind backing. Not only is there the possibility of injuring someone, but of causing property damage. Today we're going to review safety measures necessary to avoid such accidents.

SPOTTERS -AN IMPORTANT REQUIREMENT

The first requirement for safe backing is to have a spotter, someone to direct the driver. A spotter is necessary when the driver or operator does not have a full view of the backing path. This holds true for any vehicle or piece of equipment, whether it's a truck backing up or a materials truck making a delivery. This is the important rule for drivers and operators: "Don't back up unless you have a spotter directing your movement." It's an easy rule to remember.

THE SPOTTER'S RESPONSIBILITIES

The spotter has to watch out for others as well as for himself, and make sure the vehicle doesn't damage property. This may appear easy. It seems that all the spotter has to do is to direct a vehicle to back up when the path is clear of persons and objects. But there are dangers involved.

When directing the driver, stand at the rear but well to the driver's side of the vehicle. This gives you an unobstructed view of the entire backing path. And the driver can see you clearly. It's important that the driver understands your signals. So get together with the driver before any backing and explain the signals you will use. In this way you can be reasonably sure there will be no misunderstanding. Always be sure to use the same signals for the same moves. Hand signals are much better than vocal signals. Because of noise, a shouted signal may not be heard or may be misunderstood.

BE SURE YOU'RE SEEN

Always be sure that you can be seen. In addition to standing well to the driver's side of the vehicle, wear a fluorescent vest.

SPOTTERS AND DRIVERS MUST WORK TOGETHER!